## Slide 1: A Convolutional Long Shor-Term Memory-Based Approach for Predicting Missing Melt pools
Suk Ki Lee
School of Manufacturing Systems and Networks
Fatemeh Elhambakhsh
School of Computing and Augmented Intelligence
Group DMD

## Slide 2: Agenda
Problem Formulation
Pre-processing
Part 1 Methodology
Part 1 Results
Part 2 Methodology
Part 2 Results
Future Direction

## Slide 3: Problem Formulations
Additive manufacturing (AM)
  The process of joining material layer by layer manners to make the objects
  Involves intricate spatiotemporal interactions between points, lines, and layers
Melt-pool in Laser based-AM
  The areas where the laser melts the powder materials and changes their states dynamically as it moves along the designated path*
  It affects the quality and properties of the final output
Understanding the dynamics of melt-pools is important
Melt pool monitoring data can enhance our understanding of melt pool dynamics
Background
* Kruth J-P, Levy G, Klocke F, Childs T. Consolidation phenomena in laser and powder-bed based layered manufacturing. CIRP annals. 2007;56(2):730-759
Notes: In additive manufacturing, melt pool is one of the most important features.
Melt-pool is the area where the fuse process occurs in laser powder bed fusion.
It affects the quality and properties of the final outputs in AM.
That is reason why the understanding the melt pool dynamics is important
That’s why Melt pool monitoring data is also important.
It can enhance our understanding of melt pool dynamics

## Slide 4: Problem Formulations
Melt Pool Dynamics
  Melt pools have spatiotemporal dependencies between adjacent melt pools
Melt Pool Dynamics
X
Y
Layer
Scan
Direction
Notes: Melt pools have dynamical spatiotemporal dependencies between adjacent melt pools
As you can see this figure melt pools are consecutives, that means current melt pool can be affected by previous melt pools. pools

## Slide 5: Pre-processing
Preprocessing
  3 types of preprocessing: Cropping, Centering, Denoising
  Optimizes data for machine learning models, improving analysis accuracy and computational efficiency
Melt pool monitoring (MPM) images

## Slide 6: Part 1 Methodology
Capturing Spatiotemporal Dependencies
  Spatiotemporal dependency: Combines spatial (image) and temporal (time sequence) information
Why ConvLSTM?
  Spatial Patterns: Convolutional layers capture spatial features in images.
  Temporal Dynamics: LSTM layers model sequential dependencies over time.
Effective for Time-Series Data
  It works well for sequences of images, like our melt pool monitoring images
Convolutional Long Short-Term Memory (ConvLSTM)

## Slide 7: Part 1 Results
Results with pre-release data
  Missing images (left) and predicted images (right)
Missing Frame 1
MSE: 0.0037, SSIM: 0.8640
Missing Frame 3
MSE: 0.0009, SSIM: 0.9340
Missing Frame 2
MSE: 0.0012, SSIM: 0.8934
Missing Frame 4
MSE: 0.0007, SSIM: 0.9494

## Slide 8: Part 2 Methodology
Mean Squared Error (MSE) : A measure of the average squared difference between corresponding pixels in two images.
Structural Similarity Index Measure (SSIM) : A perceptual metric that quantifies image quality degradation by comparing luminance, contrast, and structure between two images.
Mutual Information (MI) : A measure of the amount of information shared between two images.
Histogram of Oriented Gradients (HOG) : A feature descriptor that captures the distribution of edge directions (gradients) in localized portions of an image.
Contextual Similarity Measurement Metrics
Notes: For second part, since there were no information about the missing images, we utilized Similarity metrics to calculate the pixel-based difference between image pairs.
We chose 4 commonly used metrics, which are mse, ssim, mi, and hog.

## Slide 9: Part 2 Results
Centered, cropped, and denoised
Centered and cropped
Cropped
MSE
Actual Location | 1 | 2 | 3
61 | 61 | 61 | 61
63 | 213 | 213 | 270
260 | 270 | 272 | 269
404 | 272 | 248 | 272
Notes: As I mentioned earlier, in the preprocessing step, we had 3 types of preprocessed images. We compared the results for each type of preprocessed image for the mentioned metrics.
Among 4 metrics and 3 preprocessed image types, mse for cropped images had the best results. Therefore, we used mse for the prediction.

## Slide 10: Future Direction
Transformer methods and their attention mechanisms show potential for examining such dependencies
  Attention mechanism